## Slide 1: Bandwidth-sharing in LHCONE
an analysis of the problem
Insert title here…

## Slide 2: Run-1 was easy
Enough CPU, disk, tape, people, coffee
Network considered a weak link
  Debugging problems considered hard
  Not clear we had enough bandwidth
  Hierarchical MONARC model
  Planned for minimal, controlled data-movement
  Data stays put, move jobs to data

## Slide 3: Run-2 will be harder
Relative reduction in CPU, disk, people
  Efficiency is becoming more important
Network now seen as more reliable
  Stable, performant, well-provisioned
  Now used as if free and infinite
Computing models: more relaxed data-placement
  T2 -> T2 transfers
  Xrootd data federations for WAN access (CMS: AAA)
  Significantly more fluid than originally planned

## Slide 4: So what’s the problem?
Data-transfer needs are growing
  Cannot assume the network will remain infinite and free forever
Computing models are evolving
  Increasingly close interaction with h/w resources
  Broader range of resource-types (opportunistic, cloud, volunteer) with different storage characteristics
Can see the value of scheduling network use
  Just-in-time data-placement, deadline management
  Possibilities that come from deterministic behaviour, not necessarily just more speed

## Slide 5: What are the solutions?
Candidate technologies, won’t discuss here
  Virtual circuits, multi-path flows
  Bandwidth guarantees can be hard or soft
  Networking groups are making progress towards a technical solution
  Successful middleware, phase 1: make it possible
Once that works, you get another problem:
  Successful middleware, phase 2: stop users abusing it!
  How do we deal with over-subscription?
  “How do we allocate bandwidth fairly & efficiently among users with different & time-dependent needs?”

## Slide 7: How not to share bandwith fairly?
Fixed quotas, static circuits?
  Inflexible, inefficient, can leave bandwidth for user X idle while user Y is maxed out (c.f. batch queues)
  Static, but needs vary by the day or by the hour
  Heavy: solution has to be implemented everywhere quotas are defined, even for when they’re not needed
  Expensive: provisioning for peaks means wasting resources at other times
  Quotas need prior negotiation, change with every new user or use-case => political heat-death

## Slide 8: What properties does a good bandwidth-sharing system have?
Automatic, lightweight
  Set up circuits automatically, but only where needed
Elastic, responsive
  Shares can grow and shrink over time
  Change on timescale of ~1 hour to follow needs
Efficient
  Allows maximal use of bandwidth at all times
  Participation not mandatory (casual or low-load users)
Fair
  Short-term &long-term, no starvation, no hogging

## Slide 9: High-level requirements: we want…
A way for users to tell LHCONE their needs
  At any time, across the whole of the LHCONE network
A way to resolve over-subscription of requests
Technology to implement the shares
  (out of scope of this talk)
Candidate solution, the Progressive Second-price Auction (PSP)
  A.Lazar, N.Semret

## Slide 10: Auctions, second-price auctions
Auction
  A vendor has something to sell, several bidders want it
  Bidders are free to choose any bidding strategy
  They may lie, collaborate, bid their true valuations…
  Auction rules decide who wins and what price they pay
  Goal may vary (maximize profit, social welfare…)
Second-price auction
  Highest-bidder wins, pays 2nd-highest bid price
  Typically less than what they think it’s worth
  Standard English auction (Sotheby’s) follows this rule

## Slide 11: Second-price auction properties
Best bidding strategy: bid your true valuation
  Bidding higher may win the auction, but you could pay more than it’s worth to you
  Bidding lower, you could lose out when the price it goes for is less than your value but more than your bid
Bidders could co-operate, force price down
  Only relevant if you’re trying to maximise profit
  Not so relevant if you’re goal is to allocate goods to those who need them most (i.e. social welfare)
Learning opponents strategy in repeated auctions
  Adaptive bidding possible, needs consideration

## Slide 12: Progressive Second-Price auction
Extends the 2nd-price auction mechanism to a divisible good, such as network bandwidth
Based on the ‘exclusion principle’:
  Allocation is based on how much is left after higher-bidding offers are satisfied
  Price based on how much was bid by bidders who are excluded because you are bidding
  Similar to progressive taxation: you pay progressively more per unit for progressively more bandwidth
  Retains truthful-bidding properties of standard 2nd-price auction

## Slide 13: How does it work?
Network offers bandwidth Q on a given link
Bidders have fixed budget (varies per bidder)
  Bidders specify a quantity and a unit-price: (qi,pi)
  PSP calculates allocation & total cost: (ai,ci)
PSP sends all allocations/costs to all bidders
Bidders revise their bids, submit them again
Repeat until convergence
Convergence guaranteed for rational bidders
  Diminishing marginal return: the more you get, the less you’re willing to pay to get even more

## Slide 14
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
Player with highest unit-price has their quantity subtracted from the total
Player with 2nd highest unit-price takes from what’s left
Bandwidth available for auction

## Slide 15
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
qi
pi
New bid ( qi, pi )

## Slide 16
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
qi
pi
New bid ( qi, pi )
How much does bidder i get?

## Slide 17
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
qi
pi
ai
How much does bidder i get?

## Slide 18
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
qi
pi
ai
How much does bidder i get?
How much does bidder i pay?

## Slide 19
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
qi
pi
ai
How much does bidder i get?
How much does bidder i pay?
ci =

## Slide 20: Some properties (NEEDS WORK)
Single bidder?
  May decide not to bother setting up a circuit if not enough competition to make it worthwhile
  Allows network to respond to sudden increase from other users if they start sending traffic
  Reduces (softens) guarantees to the single bidder who wanted the circuit

## Slide 21: PSP on multiple links?
PSP extends naturally to multiple links
  Independent auction on each link
  Bidders have fixed global budget
  Best strategy is to bid for same bandwidth on each link
  Bidder offers a price per link dependent on the competition for that link
  Can show that it still converges if bidders are rational

## Slide 22: Say something else about multiple links (NEEDS WORK)

## Slide 23: Practicalities, budgets, incentives…
How often to run the auction?
  In principle, whenever requirements change. Hourly?
  In practice, determined by policy, lifetime of circuits, capability of circuit-management s/w etc
How much bandwidth to offer?
  Can offer everything on a link
    Lets single bidder claim whole link, starve non-participants
  Can offer (e.g.) 80% of link
    Non-participants can share at least 20% of the link
    May not be able to get 100% use if only one user (unless user can bundle 80% circuit with 20% non-circuit?)

## Slide 24: Practicalities, budgets, incentives…
Real world, real money
  Budgets set by bidders
  PSP guarantees the bidders converge on a solution
LHCONE, HEP experiments
  Not real money, so who sets budgets? How?
  Initial budgets negotiated among participants
    Revise rarely, e.g. based on changes in needs
  Budget spent ~every time you win a slice of an auction
  Need topping up from time to time
  Must ensure ‘fake money’ has real value in the auction

## Slide 25: How, and how often, to update budgets?
Reset budget per-auction?
  No incentive not to spend entire budget every time
  Can lead to circuits being ‘bought’ where not needed
  Regular top-up every few hours/days/auctions?
Carry-over of unspent budget?
  Budget-hoarding => undesirable/‘unfair’ outcomes
  Carry-over with exponential decay, or similar?
Excess budget
  Blocking tactics, bidding for a link you don’t need
  Some way to penalize for under-used circuits?

## Slide 26: Conclusion
Bandwidth-sharing at LHCONE requires a mechanism for allocating bandwidth shares
  Fair, efficient, lightweight, responsive, automatic
The Progressive Second-Price auction offers this
Allows users to negotiate among themselves how much bandwidth they should each get
  Repeat auction as needs change
  Follow fluctuations in circumstances automatically

## Slide 27: Conclusion, practicalities
How much bandwidth to auction from each link
  How to deal fairly with non-participants, casual users of the network?
Using fake budget complicates things
  Setting initial budgets
  Refreshing budgets periodically
  Behaviour in repeat auctions
  Similarities to batch quotas?

## Slide 28: Backup…

## Slide 29
Q
Unit price
q4
q3
q2
q1
p4
p3
p2
p1
Allocation
qi
pi
Bidder i’s ‘utility curve’
i’s optimal bid